Functions
                              Section III.

The  TexSolver-10 numeric function set includes a wide range of operations
to help you get accurate answers with a minimum number of keystrokes.

Most of the available functions are continuously displayed on the left
side of  the screen next to a letter.   These functions are executed by
pressing the CTRL or SHIFT keys in conjunction with the respective
letter key.   For example,  to execute \f2X\f3\d010\f22\f1 (X Squared),
press CTRL-Q.   To  execute ûX (Square Root of X), press SHIFT-Q.

                      Logarithmic and Exponential

LN (SHIFT-Y). Replaces X by the natural logarithm of X.

e^X (CTRL-Y).  Replaces X by the number e to the power X.

LOG (SHIFT-U).  Replaces X by the base 10 logarithm of X.

10^X (CTRL-U). Replaces X by 10 to the power X.

                             Trigonometric

DEG (SHIFT-K). Sets degrees as the unit of angular measurement for
trigonometric functions.   When in effect, the DEG function is
highlighted in the display.

RAD (CTRL-K).  Sets radians as the unit of angular measurement for
trigonometric functions.  When in effect, the RAD function is
highlighted in the display.

GRAD (SHIFT-L).  Sets grads as the unit of angular measurement for
trigonometric functions.  When in effect, the GRAD function is
highlighted in the display. (360 degrees = 2ã radians = 400 grads).

SIN (SHIFT-G). Replaces X by the sine of X.

ASIN (CTRL-G). Replaces X by the arcsine (inverse sine) of X.

COS (SHIFT-H). Replaces X by the cosine of X.

ACOS (CTRL-H). Replaces X by the arccosine (inverse cosine) of X.

TAN (SHIFT-J). Replaces X by the tangent of X.

ATAN (CTRL-J). Replaces X by the arctangent (inverse tangent) of X.

                              Conversions

PR (SHIFT-X). Converts polar  magnitude  r and  angle é in the X and Y
registers, respectively,  to rectangular x and y coordinates placed in
the X and Y registers, respectively.

RP (CTRL-X). Converts  rectangular x and  y coordinates placed in the
X and Y registers, respectively, to polar magnitude  r and angle é
placed in the X and Y registers, respectively.

DR (SHIFT-Z) Replaces the degree value in X by the equivalent radian
value.

RD (CTRL-Z). Replaces the radian value in X by the equivalent degree
value.

HMS (SHIFT-C). Converts decimal hours (or degrees) to hours, minutes,
seconds format.  For example, 5.408600 hours will be converted to
5.243096, or 5 hours, 24 minutes, 30 seconds, and 96 hundredths of a
second.

HR (CTRL-C). Converts hours, minutes, seconds (or degrees , minutes,
seconds) format to decimal hours (or degrees). For example, 1.234567 (1
hour, 23 minutes, 45 seconds, 67 hundredths of a second) will be
converted to 1.396019 decimal hours.

                                 Math

ûX (SHIFT-Q). Replaces X by the square root of X.

X^2 (CTRL-Q). Replaces X by X squared.

1/X (SHIFT-W). Replaces X by the reciprocal of X.

Y^X (CTRL-W).  Replaces X by Y to the power X.

% (SHIFT-E). Replaces X by X percent of Y, that is, (Y * (X/100)).

%CH (CTRL-E). Replaces X by the percent of change between X and Y, that
is, ((X - Y) * 100) / Y.

ã (SHIFT-R). Replaces X by the number ã.

X! (CTRL-R). Replaces X by X factorial.

INT (SHIFT-T). Replaces X by the integer portion of X.

FRAC (CTRL-T).  Replaces X by the fractional portion of X.

                            Other Functions

PRINT (CTRL-A). When PRINT is executed, the value of X and the last
operation are printed as each operation is performed. When PRINT mode
is selected, the PRINT command on the screen is highlighted.  To turn
off PRINT mode, execute PRINT again. Make sure the printer is ready
before executing PRINT.

EXIT (CTRL-S). Saves the Stack, Storage, LAST X,  display mode, and
angular mode settings on the default drive disk file SETUPS.TS,
terminates program execution, and returns to DOS command level.

FIX (SHIFT-A). Displays numbers in fixed decimal notation.  Fixed
decimal  display is selected or modified by executing FIX (SHIFT-A)
followed  by a number from 0 to 9 to specify the number of decimal
places to which you want the display rounded. Numbers are ordinarily
displayed without exponents  unless they are too large or too small to
be displayed with the current  FIX  mode, in  which case they are
displayed  in scientific notation.  Commas are automatically  inserted
for numbers of 1,000  and greater.  In FIX mode, the FIX function is
highlighted on  the screen.

SCI (SHIFT-S). Displays numbers in scientific notation. To select SCI
mode, execute SCI (SHIFT-S) followed by a number from 0 to 9 which
specifies  the number of decimal places to which  the display is
rounded.  In  SCI mode,  the SCI function is highlighted on  the
screen.

ENG (SHIFT-D). Displays numbers in engineering notation,  which is
similar to scientific notation except all exponents are multiples of
three.  To select  ENG display mode,  execute ENG (SHIFT-D) followed by
a number  from  0 to 9 which specifies the number of additional  digits
to  be displayed after the first one.  In ENG mode,  the ENG function
is highlighted on the screen.
Note:  No matter which display mode is in effect,  numbers stored
internally are not altered.

                                 Errors

If you attempt to perform an improper operation, such as division by
zero, the LAST OP register will display ERROR.  The following
operations generate ERROR messages.

/ where X = 0.
ST/ where X = 0.
LN where X <= 0.
LOG where X <= 0.
Y^X where Y = 0 and X <= 0, or Y < 0 and X noninteger.
ASIN where |X| > 1.
ACOS where |X| > 1.
ûX where X < 0.
1/X where X = 0.
X! where X < 0.
MEAN where n = 0.
SDEV where n <= 1.
YLECC where n <= 1.
XLECC where n <= 1.
LR where n <= 1.

ERROR  is  also  displayed if division by zero or the  square  root of
a negative  number  would  be  required  during  calculation  of  the
statistical formulas.