TERM -- A Terminal Emulator for the TIPC

        Features:

                o Supports TI internal modem as well as external modems.

                o Allows storage of parameter files to automatically set
                  communication parameters for different remotes.

                o Interrupt driven communications.

                o Supports xmodem file transfer protocol for sending or
                  receiving files.

                o Allows capture of text to a file.

                o Allows definition of function keys.

                o Supports xon/xoff handshaking.

                o Supports VT100/VT52 emulation.

                o MSDOS 2.0 pathname support.

                o Easily configurable to work on different machines.

                o Has script files for automatically logging on to
                  remote systems.






























        TERM 3.00  05/26/85                                  page 1

        FOREWARD



        I  will  assume  no  responsibility for  the  program  except  to 
        fix/modify  it as I see fit.  I will not be held responsible  for 
        money,  software,  time,  etc.  lost through the use (or abuse) of 
        this  software.   I  am open to suggestions for  improvements  or 
        fixes.  I hope you enjoy using it as much as I do.

        Several  people  have helped me with my work on  TERM  -- finding 
        bugs, making suggestions, etc.  I would like to thank Ronny Horn, 
        Duane  Voth,  Marc  Newman,  and most of all my  wife  Karen  for 
        putting up with me while I work on TERM.


                        Please report any problems, complaints,
                         (praise??), to:

                                        Greg Gilley
                                        c/o BLACK BOX RBBS-RCP/M
                                        512-835-9742
                                        24hrs    300/450/1200

                        Another good place to contact me is

                                        Confusion Research Center
                                        512-471-5167
                                        24hrs    300/1200             

        I will respond as I am able.


        I  am distributing TERM as user-supported software.   This  means 
        that  I am hoping that the people who use this software will like 
        it  enough  to encourage me to continue working  on  it.   (I  am 
        easily  encouraged.)   If you get TERM off a  bulletin  board,  I 
        suggest $15.  If you cannot get it from a bulletin board, for $30 
        I  will send TERM to you on a floppy disk with a printed copy  of 
        the documentation.  Be sure to include your name and address so I 
        can send you update notices.  Please send your responses to:

                Greg Gilley
                3524 Greystone #106
                Austin,TX 78731

        I  will keep a list of users who do contribute and notify them of 
        bug fixes, new releases, new products, etc.














        TERM 3.00  05/26/85                                  page 2

        NEW FEATURES



             NOTE:  Many  of the new functions in TERM have setup  values 
                    that would not be frequently changed.   To save code, 
                    these values are not input from the standard screens.  
                    Instead,   the   configuration  file  (TERM.CFG)  and 
                    parameter  files (YOURFILE.TRM) must be  editted  and 
                    lines inserted.  Any standard text editor may be used 
                    (as  long  as it does not insert  formatting  control 
                    characters,  Wordstar  in document mode for example).  
                    Edlin  will  work fine.   In the current  release  of 
                    TERM,  it  is not acceptable to insert  extra  blanks 
                    between  the characters.   Examples will be shown  to 
                    illustrate the use of the parameters.


        Version  3.00  adds  several  new functions  to  TERM.   The  big 
        difference  is  adding  the  Modem7  and  Telink  file   transfer 
        protocols.   Modem7 is a protocol used in the CP/M world.  Telink 
        was  invented by Tom Jennings,  author of the FIDO bulletin board 
        system.   Modem7 and Telink both allow batch mode file transfers.  
        This means that wild card specifications (ie. *.exe) are allowed. 
        The  transfer proceeds until all files have  been  sent.   Telink 
        adds  the additional ability to send across exact file sizes  and 
        the  correct date and time for the file.   A side effect of these 
        new protocol additions (caused by rewriting and rethinking code),  
        is  that  the  problem with the RBBS-PC  boards  goes  away.   In 
        previous  versions  TERM  would  not  accept  the  first  end-of-
        transmission   character  it  received  and  RBBS-PC  would   not 
        retransmit.   Now,  TERM uses the number of blocks to detect when 
        an  end-of-transmission  is valid.   If you do specify  too  many 
        blocks, however, TERM will time out and close the file normally.

        Also  added  (by popular demand) is an ascii file send (F3  key).  
        It will hopefully meet most of everyone's needs.   It has options 
        which  make it relatively easy to upload messages to  editors  on 
        systems.   The  default parameters can be saved so that once  set 
        up, do not need to be reworked.

        The  F4 key will save the contents of the current screen  to  the 
        save  file.   This is for the stuff that goes by before you think 
        to hit the save key.

        The PRNT key will toggle output to the printer on and off.   This 
        will echo any characters that are received from the remote to the 
        printer (PRN).

        Direct  connection capability has been added.   It works a little 
        different than you might expect.  See the section on establishing 
        connections for an explanation.

        Answer mode has been improved (and fixed for 300  baud).  Neither 
        the answering nor the calling machine need set it in half-duplex.  
        All  echoing is handled automatically.   Still no unattended file 
        transfers though.  Maybe next time.





        TERM 3.00  05/26/85                                  page 3

        NEW FEATURES



        Added some code to do pathname validation.   I know I've typed in 
        the  wrong  names  a  few  times.   Its  operation  is  a  little 
        inconsistent with normal operation of the interface (errors  come 
        up in a window), but I'm just experimenting.

        The  function  key  definition menu is now  accessible  from  the 
        connection screen.   F7 will bring it up.  Should have been there 
        a long time ago, but some people are just born lazy.

        An  external modem initialization string has  been  added.   This 
        string  is sent once the first time the modem is used.   This can 
        be used to switch modem modes,  set ring counts,  etc.   External 
        modem support still needs work though.  No autoanswer yet.

        Abort has been added to critical error handling with some special 
        provisions for printers.  See the section on MSDOS CRITICAL ERROR 
        HANDLING for specific information.

        I'm  dropping  MSDOS  1.25 support next  release.   The  code  is 
        getting too large to justify.   Besides,  those of you who do not 
        have DOS version 2.1 should get it.  Lots of nice features.





































        TERM 3.00  05/26/85                                  page 4

        NEW FEATURES


        *** These were new features to version 2.62 ****

        Menu  selection  of  parameter files was added.   I  never  could 
        remember  all of the parameter files I had set up.   Now I  don't 
        have to.   Parameter files now require an extension of .trm.  See 
        the section on parameter files for more details.

        In  tandem  with  menu  selection  is  a  feature  I  am  calling 
        multidialing.   (Couldn't  come up with anything  better).   This 
        allows  you  to set up a list of parameter files  which  will  be 
        cycled  through.   Each parameter file will be processed until  a 
        connection  is established.   This feature comes in real handy if 
        there  are several bulletin boards that you like to  visit.   See 
        the parameter file section.













































        TERM 3.00  05/26/85                                  page 5

        BUG FIXES



        Bug Reports, Problems and Fixes
        -------------------------------
        1.  Several  people have reported problems with characters  being 
            lost when connected.   Most of the time this is the result of 
            improper  parity  settings.   On almost all of  the  bulletin 
            boards,  you can use 8 bits, strip parity bit, no parity, one 
            stop bit.   Note:  if it is an RBBS-PC board, you may want to 
            disable  parity bit stripping so you can receive the  graphic 
            characters.

        2.  CRC  checking  for the Xmodem file transfer has been  fixed!!  
            This  allows  file transfers with a 99.6% assurance  of  data 
            accuracy.   Note: some bulletin boards (most notably RBBS-PC) 
            do not support the Xmodem CRC error checking.   Check  before 
            specifying.   Xmodem  file  transfers have been  improved  in 
            general.   More  error checking has been provided yielding  a 
            more accurate transfer.

        3.  External modem support has been minimally tested with a Hayes 
            Smartmodem.  It will dial the phone for you.

        4.  There  was a problem in version 2.50 with  handling  the  300 
            baud  internal  modem.   This has now been corrected  and  it 
            should function properly. 

        5.  There   was  a  pretty  bad bug in  version  2.60  with  file 
            receive.   If no receive path was specified, a critical error 
            would occur.  This is now fixed.

        6.  Autoanswer at 300 baud was not working.  It should now.

        7.   Literal  characters specified with the 'C'-type syntax  (ie. 
             \x00)  were  not working properly.   Actually  some  of  the 
             values  were  but  most  were not.   Thank  the  C  operator 
             precedence (and my oversight) for that. 























        TERM 3.00  05/26/85                                  page 6

        KNOWN PROBLEMS



        Problems/Incomplete functions in TERM
        -------------------------------------

        1.  VT100/VT52 emulation.
            The VT100/VT52 emulation  is incomplete.    Most of the major 
            functions are implemented.  It has been expanded to the point 
            that the EDT editor on a VAX will work properly.   If you use 
            it and find a problem, please let me know so I can fix it.   

        2.  Errors.
            TERM  does not do a great deal of error  checking.   Since  I 
            know it inside-out,  I do not need much error checking.   But 
            in  the interest of other users,   I will attempt to  improve 
            error handling.

        3.  MSDOS 1.25/2.0 support.
            MSDOS  2.0  support works well.   It is what I normally  use.  
            MSDOS 1.25 support has not been tested thoroughly.  It should 
            work.







































        TERM 3.00  05/26/85                                  page 7

        FUTURE PLANS



        FUTURE PLANS
        ------------

        TERM is sort of my pet project.   My personal version undergoes a 
        great many changes.  I will try to keep new releases organized to 
        protect your sanity.

        I hope to add sometime (in addition to bug fixes):
            Full VT100/52 emulation.
            Kermit file transfer protocol support.
            More error checking.
            Sustained (long) BREAK transmission.
            Automatic script file generation.

        I will not release source code any time soon.  Please, don't ask.











































        TERM 3.00  05/26/85                                  page 8

        TERM


        TERM is a general purpose communications program.   It began as a 
        simple  TTY emulator and has since been hacked-up,  added-to  and 
        (hopefully)  improved.   TERM is loosely modeled around COMTTY to 
        make it easier to use for those people who already own COMTTY.

        An  attempt was made in TERM to provide a  consistent  interface.  
        Pressing  F12  will  abort  you  out  of  most  anything.    When 
        information  is  required from the user,  it is usually  elicited 
        through  a "window".   See the EDITING FEATURES section for  more 
        information on input.

        When  TERM is executed,  it checks for the existence of  a  file 
        called  TERM.CFG.   It  reads  information about  the  particular 
        machine it is running on from this file:  which comm port to use, 
        where files should go,  etc.   If this file does not exist,   the 
        program  automatically  switches to the  SET  TERM  CONFIGURATION 
        menu.   Otherwise,  the main screen comes up.  When bringing TERM 
        up, a parameter file can be specified if desired.  The command

          TERM filename

        will attempt to connect to the parameter file "filename".

        An  environment variable can be set (in MSDOS 2.0) to  tell  TERM 
        where  the  file  TERM.CFG is located.   This allows TERM  to  be 
        executed from any drive or from any subdirectory.   The  variable 
        is called TERMCFG.  Just issue the command

             set TERMCFG=e:\usr\term     (your subdirectory) 

        from  the  MSDOS prompt (or in a batch  file).   TERM  will  then 
        search   the   environment  to  find  TERMCFG  and   locate   the 
        configuration file.


























        TERM 3.00  05/26/85                                  page 9

        MAIN SCREEN


        MAIN SCREEN
        -----------

        The  main screen comes up with a title,  and a status line across 
        the bottom of the screen.   The status line Documents which func-
        tions are available and which function key to press.

        F2:Setup     -- Takes  you  to  the parameter  setup  menu  which 
                        allows  parameter files to be initialized.   This 
                        must   be   done  before   connections   can   be 
                        established.

        F3:Start     -- Starts  the  connection  sequence.    A  menu  of 
                        parameter files pops up.   Use the arrow keys  to 
                        move  the  cursor on to the name of  the  desired 
                        parameter file.   If a character is pressed,  the 
                        cursor  will be moved to the first parameter file 
                        with  that character as the first letter  of  its 
                        name.    Press  the  RETURN  key  to  select  the 
                        parameter file.  TERM then attempts to connect to 
                        the remote system.

                        To  initiate multidialing,  the procedure is much 
                        the  same.    Move  the  cursor  to  the  desired 
                        parameter  file  and press  the  space  bar.   An 
                        asterik   (*)   will  appear  beside  the   name.  
                        Pressing  the  space  bar on  a  name  which  has 
                        already  been selected will deselect  it.  Repeat 
                        this procedure until the desired set of names (up 
                        to 10) is selected.  Pressing the RETURN key will 
                        start the multidialing.  Each parameter file will 
                        be  processed until a connection is  established.  
                        There  is  no time limit placed on  multidialing.  
                        If it cannot get a connection,  it will dial  all 
                        night!
                            
        F5:Reconfigure  -- Takes you to the set TERM configuration  menu.  
                        Allows  configuration  parameters (screen  color, 
                        port,  etc.)  to be changed.   The  configuration 
                        file   (TERM.CFG)   is  updated  with   the   new 
                        information.

        F8:DOS       -- Puts  you  in MSDOS without having to  exit  TERM 
                        first.   Typing  EXIT in MSDOS will return you to 
                        TERM.

        F12:Exit     -- Exit TERM and return to MSDOS.












        TERM 3.00  05/26/85                                  page 10

        CONFIGURATION


        SET TERM CONFIGURATION
        ----------------------

        When this screen comes up,  there will be an initial delay.  This 
        is because TERM is checking the machine for the existence of comm 
        boards  and  internal  modems.   The boards that  exist  will  be 
        displayed.  The parameters that are to be specified follow:


        Port Number
        -----------
        This parameter is in the range 1 to 4 and will specify which comm 
        port  will be used by TERM.   The list of installed comm  boards/ 
        modems  is given to make selection easier.   TERM  will  automat-
        ically  determine  if  the chosen port is an internal  modem.

        Status Intensity
        ----------------
        This is the intensity (on a monochrome monitor) or color for  the 
        status line which appears at the bottom of the screen.  It may be 
        set to blue, red, magenta, green, cyan, yellow, or white.

        Display Intensity
        -----------------
        This  is the intensity (on a monochrome monitor) or color for the 
        display portion of the screen.   All characters received will  be 
        displayed   in  this  color  (unless  changed  by  the   received 
        characters).

        Default Pathspec for File Receives
        ----------------------------------
        This  is  the  pathspec (MSDOS 2.0) or drive (MSDOS  1.25)  which 
        gives the destination of files which are downloaded using TERM.
        Example:
           MSDOS 2.0:
                Default Pathspec for File Receives   : e:\usr\comm\recv\
           MSDOS 1.25:
                Default Pathspec for File Receives   : a:

        Default Pathspec for File Transmits
        ----------------------------------
        This  is  the  pathspec (MSDOS 2.0) or drive (MSDOS  1.25)  which 
        gives the source location of files which are uploaded using TERM.
        Example:
           MSDOS 2.0:
                Default Pathspec for File Transmits  : e:\usr\comm\send\
           MSDOS 1.25:
                Default Pathspec for File Transmits  : b:











        TERM 3.00  05/26/85                                  page 11

        CONFIGURATION


        Default Pathspec for Parameter Files
        ------------------------------------    
        This  is  the pathspec (MSDOS 2.0) or drive  (MSDOS  1.25)  which 
        gives  the  location  of the parameter files which TERM  uses  to 
        store information on the remote systems.
        Example:
           MSDOS 2.0:
                Default Pathspec for Parameter Files : e:\usr\comm\param\
           MSDOS 1.25:
                Default Pathspec for Parameter Files : a:

        Default Save filename
        ---------------------
        This is the filespec (including drive and/or MSDOS 2.0  pathspec) 
        for the default save file.  TERM allows received characters to be 
        saved  in a file.   This is the file which will be used each time 
        TERM is executed.   If the file already exists,  TERM will append 
        the new data to the existing file.
        Example:
           MSDOS 2.0:
                Default Save filename : e:\usr\comm\term\term.sav
           MSDOS 1.25:
                Default Save filename : a:term.sav

        Dialing (M)anual (A)utomatic
        ----------------------------
        If  an internal modem is being used,  TERM can automatically dial 
        the  number and connect to the remote.   If an external modem  is 
        used which uses ASCII commands to dial, TERM can dial it as well.

        Dial type (P)ulse (T)one
        ------------------------
        Selects dialing mode for TI internal modem.   Note that this mode 
        can  be switched during dialing by placing a 'T' for tone dialing 
        or a 'P' for pulse dialing in the phone number. (See phone number 
        under paramter setup).

        Redial Delay
        ------------
        If  a  TI internal modem is being used,  TERM  can  automatically 
        retry to dial a number.   The redial delay specifies the time (in 
        seconds) to wait before attempting to dial the number again.

        Modem Autodial control string
        -----------------------------
        This  prompt  will only appear if a non-TI modem is  being  used.  
        This is the control string that causes the modem to dial.  On the 
        Hayes-type  modems,  this is 'ATDT' (no  quotes).   'C'  language 
        control strings may be entered (See appendix A).

        Number of bells to ring after connection
        ----------------------------------------
        This  was  added to aide those who set redial on 999 and go  have 
        lunch.   This will ring the bell the number of times specified or 
        until  a key is pressed.   There is a half-second  delay  between 
        each bell.



        TERM 3.00  05/26/85                                  page 12

        PARAMETER SETUP


        PARAMETER SETUP
        ---------------

        Parameters are stored in files and include information needed  by 
        TERM  for  connecting  to each  computer.   Information  that  is 
        variable  from  computer to computer  (baud,  parity,  etc.)  are 
        stored in these files.   To access the parameter file setup menu, 
        press  the F2 key on the main menu.

        A menu of the available parameter files pops up.   Use the  arrow 
        keys  to  move the cursor onto the desired parameter file  or  to 
        <NEWFILE> if no initial parameters are desired.  Press the RETURN 
        key to select the parameter file.  Now a menu screen comes up.

            NOTE:  Parameter files now have a required extension of .trm.  
                   To  make old parameter files available,  simply rename 
                   them to have an extension of .trm.  For example, if no 
                   extension was used previously, then the command

                   ren *. *.trm

                   should make all the old parameter files available.


        Parameters      -- Puts up a parameter setup window which  allows 
                           specifying    parameters    for     individual 
                           connections.

        Function Keys   -- Allows the user to  access  the  function  key 
                           definition screen.

        Save Parameters -- The filename specification for  the  parameter 
                           file.  This will be used when the start option 
                           is  selected from the main screen.   Unless  a 
                           path/drive  is  specified  explicitly  in  the 
                           filename,  the default parameter pathspec from 
                           the configuration will be used.


        When   the  parameter  setup  window  comes  up,   the  following 
        information will be elicited:

        Description
        -----------
        A thirty character description of the destination computer  which 
        is displayed when an attempt is made to connect.

        Baud Rate
        ---------
        The baud rate for the connection.   If an internal modem is used, 
        the modem is automatically switched to 1200 baud if selected.








        TERM 3.00  05/26/85                                  page 13

        PARAMETER SETUP


        Parity
        ------
        Allows selection of no parity,  odd,  even, mark or space parity.  
        The  best  parity  setting (will work with most  systems)  is  no 
        parity.

        Strip Parity Bit
        ----------------
        This  is used to strip the parity bit (bit 7) off incoming  bytes 
        before   they  are  displayed.    This  does  not  affect  xmodem 
        transfers.   On non-RBBS-PC boards,  it is best to strip off this 
        bit.   In many cases,  the remote system may be sending data with 
        parity checking.

        Wordsize
        --------
        Number of bits in a data word (7 or 8).  The best value to use is 
        8 bits.

        Stopbits
        --------
        Number  of  stopbits in a data word (1 or  2).   The  recommended 
        value is 1 stopbit.

        Busy Handling
        -------------
        Allow connecting system to halt output from your system and vice-
        versa.   Helps  to prevent data from being lost.   Xon-Xoff (DC1-
        DC3)  handling  is  supported.   This  feature  is  not  normally 
        supported on microcomputer based bulletin boards.  However, large 
        systems such as Compuserve do use xon/xoff busy handling.

        Terminal Type
        -------------
        The type of terminal to be emulated:   tty (normal mode),  VT100, 
        or VT52.   At this time,  this emulation is incomplete.  (See the 
        TERMINAL EMULATION section for a list of supported features).  On 
        some  RBBS-PC  bulletin boards,  "ANSI graphics"  are  supported.  
        This  is  equivalent to VT100 on TERM.   Note  that  for  graphic 
        characters  to be displayed properly,  the settings should be  no 
        parity, do not strip parity bit, 8 data bits and 1 stop bit.

        Phone
        -----
        The  phone  number  for  the  remote  computer.    Digits  (0-9), 
        separator (-), wait for dial tone (+), pause for two seconds (@), 
        phone  control (#,*),  tone dialing mode (T),  and pulse  dialing 
        mode (P) are supported.   Note that the preceding characters  are 
        for  use with a TI internal modem only.   If an external modem is 
        used,  insert the appropriate control characters for that  modem.  
        Control  characters (non-displayable) may be specified in the 'C' 
        programming language format.  A backslash followed by a 'b', 'r', 
        'n',  etc. or and x and a two-digit hexadecimal number (ie., \x0b 
        for a form feed).  See appendix A.





        TERM 3.00  05/26/85                                  page 14

        PARAMETER SETUP


        Example:
                If your home phone is pulse (rotary) dialing then  select 
                pulse dialing mode during Configuration setup.   To use a 
                service  such as Sprint or MCI the phone number would  be 
                similar to the following:

                Phone number : 5551313+T123456789+1235558989

                The first number is the local number of the service.  The 
                '+'  waits  for a dial tone.   The 'T' switches  to  tone 
                dialing  (required  for  most  services).   The  password 
                (account  number)  follows and then another  pause.   The 
                final number is the telephone number desired.

        If  the phone number is omitted then TERM will answer the  phone.  
        This  mode  is not intended for unattended operation so  it  will 
        only  answer one call.   This allows two users to transfer  files 
        without an RBBS type program. 









































        TERM 3.00  05/26/85                                  page 15

        ESTABLISHING CONNECTIONS



        ESTABLISHING CONNECTIONS
        ------------------------
        TERM  has two modes of connections,  through a modem and directly 
        to  another  machine.   If  a  modem  is  being  used,  TERM  can 
        automatically dial the number if the modem supports it.

        For  an  internal modem,  simply specify the  phone  number  when 
        setting  up  the parameters.   See phone number  under  parameter 
        setup.

        For  an external modem,  a little more work is required.   If the 
        modem  requires initialization,  an initialization string can  be 
        specified in the configuration file.  To set this value, edit the 
        configuration file (TERM.CFG).  Add the line:

        eis=Q1

        where  anything  following the equal sign is sent  to  the  modem 
        before  any numbers are dialed.   The characters may include  the 
        'C' language convention shown in appendix A.

        The modem autodial control string in sent immediately before each 
        phone  number.   For  Smartmodem compatible modems this would  be 
        'ATDT' for tone dialing and 'ATDP' for pulse dialing.   See phone 
        number under parameter setup.

        For a direct connection,  a different sort of setup is used.   To 
        allow  the use of a modem in conjunction with a direct connection  
        without having to change the configuration every time,  an  entry 
        in the parameter file is used.   To specify the direct connection 
        port,  the "override port",  edit the parameter file (just set it 
        up normally first) and specify:

        opo=1

        where  the number specified is the comm port number.   This  port 
        number is in effect only for the duration of this connection.
              
        All  connections begin the same general way.   The Start key (F3) 
        is  pressed on the main menu.   Then a parameter file  which  was 
        created  using  the  parameter  setup  menu  is  selected.   This 
        selection  can take place in two ways.

        The  first way is to move the arrow keys and position the  cursor 
        over  the name of the desired parameter file.   Press the  RETURN 
        key  to  select the name.   At this point,  TERM will  begin  the 
        connection process.   If the file selected had the override  port 
        line  included  (is  a direct  connection),  then  connection  is 
        immediate  and  the terminal mode screen should appear.   If  the 
        parameter  file was not set up for direct connection,  then  TERM 
        should start the dialing process.







        TERM 3.00  05/26/85                                  page 16

        ESTABLISHING CONNECTIONS



        The  dialing  process  has a screen  which  monitors  the  call's 
        progress.   This  screen  is  really only active  when  using  an 
        internal modem.   It shows the current state of dialing: dialing, 
        ringing, busy, etc.  It shows the amount of time remaining before 
        the call is aborted.  Finally it shows the number of call retries 
        remaining.

        If  a  connection fails for whatever  reason  (busy,  no  answer, 
        etc.),  TERM will bring up a pop-up window and ask if you want to 
        retry to establish the connection.  If no is answered, control is 
        returned to the main menu.   If yes is selected,  TERM puts up  a 
        pop-up window and prompts for the following information:

        Number of call retries (0-9999)
        -------------------------------
        This  specifies  the  number of tries that TERM  should  make  to 
        establish a connection before giving up.

        Timout after dialing waiting on a ring (1-30)
        ---------------------------------------------
        This  delay  specifies the number of seconds that TERM will  wait 
        before aborting a connection attempt.   20 seconds is the default 
        valued used when TERM tries to connect the first time.   If  TERM 
        detects  a ring,  it will reset the timeout counter to this value 
        to allow extra time to establish the connection.


        The  second  way to select parameter files also initiates  multi-
        dialing.   This  method  allows a list of parameter files  to  be 
        contructed.   TERM  will  then  sequence through  this  list  and 
        attempt to connect to each system.  It will continue to try until 
        a connection is established,  or until it is aborted.   To set up 
        multi-dialing,  use  the  arrow keys to place the cursor  on  the 
        desired  parameter  file.   Press  the space bar  to  select  the 
        parameter file.   An asterik (*) will appear beside the filename.  
        The  parameter file can be deselected by pressing the  space  bar 
        again.   When  all parameter files have been selected (up to 10), 
        press the return key to start the dialing process.




















        TERM 3.00  05/26/85                                  page 17

        TERMINAL MODE



        TERMINAL MODE
        -------------

                Once connection to the remote has been established,  TERM 
        clears the screen and prints a "Connected to" message followed by 
        the Description specified in parameter setup.
                A status line is displayed across the bottom of the
        screen.  It shows what functions are available on which key.

        F1:Sav   -- TERM allows saving received characters to a file.  F1
                    toggles saving on and off.

        F2:NuSav -- Allows the text saved by F1 to be saved in a file
                    other than the one specified in the configuration
                    section.

        F3:AscSnd -- Send an ASCII format file.  Should be used only when
                    xmodem   transfers   are  unavailable  or   are   not 
                    appropriate as when uploading messages to a bulletin
                    board system.

        F5:Recv  -- Download a file using the xmodem protocol.  This
                    key takes you to a screen where parameters are
                    specified.

        F6:Send  -- Upload a file using the xmodem protocol.  This key
                    takes you to a screen where parameters are specified.

        F8:DOS   -- Goto MSDOS.  This feature works only under MSDOS 2.1+.
                    It allows you to get into MSDOS and perform functions
                    such as directory, etc. without disconnecting.

        F9:Time  -- Displays time elapsed since connection was established.

        F10:Parms-- Allows changing the communication parameters while
                    connected. (Baud, parity, etc.)  Use with discretion!

        F12:Abort-- Disconnect from remote.

        Other  keys  which  have functions in this  mode,  but  were  not 
        documented on the status line because of space limitations are:

        F4       -- Saves  the  contents  of the current  screen  to  the 
                    current  save file.   This is used when something has 
                    come  up on the screen before the save key (F1) could 
                    be pressed.

        PRNT     -- Toggles output to the printer (PRN) on and off.   The 
                    characters that are received from the remote are sent
                    to the printer as well.

        BRK      -- This  key  will send a short  break  to  the  remote 
                    system.  This is recognized as an "attention key" by
                    some systems.  (Most UNIX systems for example).
                 



        TERM 3.00  05/26/85                                  page 18

        EDITING FEATURES



        COMMAND LINE EDITING FEATURES
        -----------------------------

        When TERM prompts for information, a number of keys are available 
        for  editing  the line.   The left and right arrow keys  do  non-
        destructive cursor movement.   Backspace will delete  characters.  
        INS  will  start  insert mode -- characters are inserted  at  the 
        cursor.  The cursor changes shape to indicate the mode.   A  full 
        cursor shows overtype mode;  a half cursor shows insert mode. DEL 
        will delete a character at the cursor.   SHIFT-DEL will delete to 
        the end of the line.  SHIFT-left arrow will move to the beginning 
        of the line. SHIFT-right arrow or TAB will move to the end of the 
        line.  RETURN will end the editing.

        Whenever you are in a "window" answering prompts, the up and down 
        arrow  keys  can  be used to move back and forth (up  and  down?) 
        between  the items.   If the arrows will not move you,  then  the 
        value  is illegal or the value is required and you must  make  an 
        input.


        MS-DOS CRITICAL ERROR HANDLING
        ------------------------------

        TERM  will allow you to recover from MSDOS critical errors  in  a 
        way  that  is a little more aesthetically pleasing than  the  way 
        Command.com handles them. An error screen is shown when the error 
        occurs.   This  is  a  replacement for the all too  familiar  DOS 
        prompt of Abort,  Retry, Ignore.  In most cases, you will want to 
        specify  Retry  or  Ignore.   Press the R key or  the  I  key  to 
        accomplish this.   In some instances, however, the only available 
        option is to Abort.  Press the A key to accomplish this.

        Under  DOS 2.0,  aborting a critical error will cause the current 
        program to be terminated and control returned to DOS.   If  abort 
        is selected,  TERM will clean up before DOS terminates it so that 
        you  will not have to reboot your system.   If the critical error 
        involved the printer,  ie.  printer not ready,  then the PRNT key 
        toggle will be turned off and control returned to TERM.   This is 
        so  that if the PRNT key is accidentally pressed and you  do  not 
        have a printer, you will not have to abort your current session.

















        TERM 3.00  05/26/85                                  page 19

        SCRIPT FILES


        SCRIPT FILES
        ------------

        Script  files are used for automatically logging on to  a  remote    
        system.   They  can also be used to automatically download  files 
        unattended.  The  script file is located in the same directory as 
        the  parameter files.   The script file has the same name as  the 
        parameter file with a .spt extension.  The script file is created 
        with  any  text editor.   The script file will  automatically  be 
        executed  unless a -n is specified on the command line when  TERM 
        is executed.  During the processing of script files, pressing F12 
        will  abort  the  script.   You will still be  connected  to  the 
        remote.

        Script File Commands
        --------------------

        Alarm     --  Ring the bell.

        Cls       --  Clear the text screen.

        Close     --  Stop output to a save file and close it.
                      Ex.  close

        Delay     --  Delay in milliseconds between sending characters.
                      Default is no delay. A delay of 0 means no delay.
                      Ex.  delay 50

        Do        --  Execute another script file.   Recursion up to  ten 
                      levels is supported.   The file name extension must 
                      be .spt.
                      Ex.  do "RBBSPC"

        Limit     --  This is the number of hundredths of a second  after 
                      characters  stop coming which will cause a match to 
                      fail.  The default is 20 seconds (2000 hundredths).
                      Ex.  limit 200

        Match     --  Match a string.   If this string is  received  then 
                      the  match succeeds.   Note that this command  does 
                      not  care about the context of the string.   If you 
                      match "new" then it will also match  "renew",  etc.  
                      LIMIT  controls the timeout of this command.   Case 
                      of characters is significant. 
                      Ex. match "more (y/n)"

        Output    --  Turns  the  output  of received  characters  during 
                      script processing on or off.   Arguments are ON  or 
                      OFF.
                      Ex.  output on









        TERM 3.00  05/26/85                                  page 20

        SCRIPT FILES


        Prompt    --  Match  a  prompt string.   It is assumed  that  the 
                      string to be matched is a prompt.   In other words, 
                      a  sequence  of characters is received and  then  a 
                      pause waiting for user input.   LIMIT and THRESHOLD 
                      control  the  timing  of  this  command.   Case  of 
                      characters and blanks are significant.

                      Ex.  prompt "username: "


        Rem       --  When  script output is on,  this line does nothing.  
                      When script output is off,  this line is  displayed 
                      in  a  pop-up window until another rem  command  is 
                      encountered or until the script ends.  This is very 
                      useful  to  show the status of script files  during 
                      autologon.
                      Ex.  rem "*** Verifying Password ***"

        Save      --  Open  a save file and start output.   The  default
                      path is the receive path.
                      Ex.  save "e:/usr/comm/term/term.sav"

        Send      --  Send  a string.   Control or special characters can 
                      be  entered  using  the  'C'  programming  language 
                      conventions.  A backslash (\) followed by an r (for 
                      return),  b (for backspace),  t (for tab),  or an x 
                      followed  by  a two-digit hexidecimal  number  (ie. 
                      \x0b for form feed).  See appendix A.
                      Ex.  send "Greg Gilley\r"

        Sende     --  Send a string and wait for echo of each char.  This 
                      command  does  not  check if the  echoed  character 
                      matches the one sent and could be used in the  case 
                      of  passwords when dots,  etc.  are  echoed.   This 
                      command  allows  pacing with the target system  and 
                      helps  to  insure that you do not  send  characters 
                      faster than it can receive them.
                      Ex.  sende "54001,234\r"

        Threshold --  This  command is used in conjunction with the MATCH 
                      command.  While match is waiting for a prompt, this 
                      is the amount of time to wait after characters stop 
                      coming from the remote before testing for a  match.  
                      The time is specified in tenths of a second.
                      Ex.  threshold 20 

        See  appendix  A  for an explanation of characters which  can  be 
        placed in a script string.











        TERM 3.00  05/26/85                                  page 21

        SCRIPT FILES


        Example script files:

           This is a script file that I use for RBBS-PC type boards.

        output off
        rem  "*** Connecting to Deep Thought ***"
        pause 1000
        send "\r"
        pause 1000
        send "\r"
        rem  "*** Answering useless prompts ***"
        prompt "CASE? "
        send "y\r"
        prompt "graphics? "
        send "y\r"
        prompt "Name? "
        rem   "*** Sending name ***"
        sende "FIRST\r"
        match "Name? "
        sende "LAST\r"
        match "echo)? "
        rem   "*** Sending Password ***"
        sende "PASSWORD\r"

        Just  replace  FIRST with your first name,  LAST with  your  last 
        name, and PASSWORD with you password.

            Here is one that I use for COMPUSERVE(tm).

        output off
        rem  "*** Connecting to Compuserv ***"
        pause 3000
        send "\x03"
        prompt "User ID: "
        rem  "*** Sending user id ***"
        sende "USER,ID\r"
        rem  "*** Sending password ***"
        prompt "Password: "
        send "PASSWORD\r"
        pause 3000
        match "!"

        Replace  USER,ID  with  your  user  id,  and  PASSWORD  with  you 
        password.   You  could  even  add commands to send  you  to  your 
        favorite SIG.














        TERM 3.00  05/26/85                                  page 22

        FILE TRANSFERS



        FILE TRANSFERS
        --------------
        TERM  supports  several file transfer protocols.   All  of  these 
        transfers  are  based on the xmodem transfer protocol  originally 
        devised by Ward Christenson.  The xmodem protocol allows transfer 
        of  files with error correction.   It allows single files  to  be 
        transferred  between systems and is almost universally supported.  
        Modem7  is  an  extension of xmodem and allows  batch  mode  file 
        transfers.   This means that multiple files can be sent with  one 
        command (*.exe for example).   Modem7 is supported mainly on CP/M 
        based bulletin boards.   Telink is an extension to modem7 done by 
        Tom Jennings, author of the FIDO bbs system.  It allows the batch 
        file  transfers but also transfers file information.   File size, 
        date,  and time are all sent across so that the received file  is 
        virtually identical to the original.   Telink is supported on the 
        FIDO bulletin board system.
          
        TERM  supports  CRC (cyclic redundancy check) error  checking  as 
        well  as  the standard checksum error  checking.   Some  bulletin 
        boards do not support the CRC type of error checking.  Check with 
        the  system operator of the board before trying.   Boards that do 
        support CRC checking are Compuserve,  FIDO,  and most CP/M  based 
        systems.   Boards  that do not support CRC checking are  RBBS-PC, 
        TBBS, and NOCHANGE.

        TERM reports and keeps count of errors during file  transmission.  
        If  an  error  occurs,  TERM will either resend the block  or  if 
        receiving,  will  request a retransfer.   The NAKed blocks  count 
        shows  the  number of errors during a send.   The  Error  Packets 
        count shows the number of errors during a receive.

        The  error  count  is  given only as an  indication  of  how  the 
        transfer is proceeding.   If too many errors are  occurring,  you 
        may  wish to abort the transfer (via F12) and retry again  later.  
        When receiving, if ten errors occur in a row, TERM will abort the 
        transfer.   The  connection  is simply too poor to  facilitate  a 
        transfer.

        TERM  is set up to make file transfers with the highest  possible 
        throughput.   This  causes  problems  for some  systems  such  as 
        mainframes  where  long  delays between characters  sent  by  the 
        mainframe can cause synchronization problems.  TERM allows you to 
        modify  the  timing parameters to allow transfers to  occur  with 
        these systems.   To change them,  edit the parameter file and add 
        two lines:

        xm_char=10
        xm_block=20

        (Please  do  not  put spaces between  the  characters.)   Xm_char 
        specifies maximum delay between characters in seconds.   Xm_block 
        specifies  maximum delay between blocks in seconds.   The  values 
        shown are the ones I use for Compuserve.   The default values are 
        xm_char=1 and xm_block=10.




        TERM 3.00  05/26/85                                  page 23

        FILE TRANSFERS


        When   a  receive  is  started,   most  systems  will  tell   you 
        approximately  how  long  the transfer will  take  and  how  many 
        "sectors"  (or "blocks") the file takes.   You can use the number 
        of  sectors to help you keep track of the  transfer.   Enter  the 
        number  of sectors at the prompt when setting up a file  receive. 
        If you do not know the number of sectors, but do know the size of 
        the file, then enter the size of the file in bytes followed by an 
        'L' (ie.  34567L).  TERM will calculate the number of sectors for 
        you.   TERM will also check the amount of disk space available on 
        the disk and determine if there is room for the file.

        There  is an internal buffer that TERM uses for storing  sections 
        of  the  file  as  it is being  transmitted.   TERM  buffers  the 
        incoming and outgoing sectors to reduce the amount of time  spent 
        accessing  the disk during a transfer.   The default size of this 
        buffer is 16K bytes.  This size is good for floppy-based systems, 
        but   not   really  necessary  for  winchester   based   systems.  
        Winchester  users may want to reduce the size of this buffer  and 
        allow TERM to run in a smaller amount of memory.   To change this 
        buffer,  edit  the  configuration  file (TERM.CFG)  and  add  the 
        following line:

        bufsize=4096

        (please do not put extra spaces).   This will set the buffer size 
        to 4K.   You can set it to any value and TERM will round it to  a 
        multiple  of  128 (the size of a block during transfer).   It  is 
        recommended  that the size does not exceed 32K bytes.   Users  of 
        systems  with  128K memory may need to reduce the  size  of  this 
        buffer to get TERM to run.           





























        TERM 3.00  05/26/85                                  page 24

        ASCII FILE TRANSFERS



        ASCII FILE TRANSFERS
        --------------------

        ASCII file transfers are generally more difficult to achieve than 
        xmodem  based  transfers.   The  xmodem   file  transfer  protocol 
        includes  handshaking to keep the computers from sending data too 
        quickly  to  each  other.   If both  computers  support  xon/xoff 
        handshanking,  this makes ASCII file transfers easier.   But most 
        microcomputer  bulletin board systems do not support it,  so  the 
        burden  of  regulating  data flow falls on  the  system  that  is 
        sending the data.

        TERM  is set up to allow ASCII files to be sent to another system 
        under most conditions.   A number of conditions are changeable to 
        allow pacing with the remote system.

        When  ASCSND  is selected (F3 key),  TERM brings up  a  menu  and 
        prompts for the following information:

        Wait for character echo (y/n)
        -----------------------------
        Answering  yes  will cause TERM to wait for the echo of the  last 
        character sent before sending the next one.  This option will cut 
        the  effective  speed  of the transfer in  half,  but  is  almost 
        essential for systems which do not allow type-ahead.

        Delay between characters (msecs)
        --------------------------------
        This parameter specifies the delay in milliseconds that TERM will 
        pause after sending a character before sending the next one.

        Delay after sending eol (msecs)
        -------------------------------
        TERM  breaks  ASCII files into their logical  components,  lines, 
        while  sending  them.   This  parameter specifies  the  delay  in 
        milliseconds  that TERM pauses after sending the  end-of-line  to 
        the receiving system.

        EOL string (CR)
        ---------------
        This  parameter specifies the characters that will be sent to the 
        receiving  system to indicate end-of-line.   TERM will  intercept 
        carriage return/linefeed sequences and send this string in  their 
        place.   The default value is carriage return only.  See appendix 
        A for valid characters.

        Prompt after EOL
        ----------------
        This  is the string that the receiving system uses to prompt  for 
        the  next line.   TERM will wait for this prompt after sending an 
        end-of-line sequence.







        TERM 3.00  05/26/85                                  page 25

        ASCII FILE TRANSFERS


        View data (y/n)
        ---------------
        This allows the data to be viewed as it is being transmitted.


        While the transfer is in progress,  TERM will display a  flashing 
        message  in  the  status  line  to  indicate  that  something  is 
        happening.



















































        TERM 3.00  05/26/85                                  page 26

        TERMINAL EMULATION



        Escape Sequences Supported
        --------------------------
        The following escape sequence in VT100 mode are supported (wholly 
        or in part):

               ESC 7           Save cursor position and attribute
               ESC 8           Restore cursor position and attribute
               ESC D           Move down one line in region
               ESC E           Beginning of next line in region
               ESC H           Horizontal tab set
               ESC M           Move up one line in region
               ESC Z           Status reports (returns ESC [?1;0c )
               ESC c           Reset terminal
               ESC =           Alternate keypad mode
               ESC >           Numeric keypad mode
               ESC (0          Graphics primary character set
               ESC (A          UK primary character set     
               ESC (B          US primary character set
               ESC )0          Graphics secondary character set
               ESC )A          UK secondary character set     
               ESC )B          US secondary character set
               ESC [ Pl;Pc H   Position cursor
               ESC [ J         Erase to end of screen
               ESC [ 0 J       Erase to end of screen
               ESC [ 1 J       Erase to beginning of screen     
               ESC [ 2 J       Erase entire screen
               ESC [ K         Erase to end of line
               ESC [ 0 K       Erase to end of line
               ESC [ 1 K       Erase to beginning of line
               ESC [ 2 K       Erase entire line
               ESC [ Pn L      Insert line
               ESC [ Pn M      Delete line
               ESC [ PN P      Delete character
               ESC [ Pn c      Status reports (returns ESC [?1;0c )
               ESC [ Pl;Pc f   Position cursor
               ESC [ g         Horizontal tab clear (current column)
               ESC [ 0 g       Horizontal tab clear (current column)
               ESC [ 3 g       Clear all tabs
               ESC [ Pn h      Set mode (see modes below)
               ESC [ Pn l      Reset mode (see modes below)
               ESC [ Pn m      Set attributes (0-default, 1-bold,
                                   4-underline, 5-blink, 7-reverse,
                                   30-black, 31-red, 32-green, 33-yellow,
                                   34-blue, 35-magenta, 36-cyan, 
                                   37-white)
               ESC [ 5 n       Status report (returns ESC 0n)
               ESC [ 6 n       Report cursor position
               ESC [ Pt;Pb r   Define scrolling region










        TERM 3.00  05/26/85                                  page 27

        TERMINAL EMULATION


        The modes which are supported by this emulator and can be set  by 
        the  Set  mode  sequence  and reset by the  Reset  mode  sequence  
        include the following. 

                    ?1  Cursor key mode
                    ?2  VT52 mode (Reset mode only)               
                    4   Insert character mode
                    ?5  Reverse screen               
                    ?6  Origin mode
                    ?7  Auto wrap mode
                    ?8  Auto repeat
                    20  Newline mode



        In VT52 mode, the following escape sequences are supported:


               ESC <           Enter ANSI (VT100) mode
               ESC =           Enter alternate keypad mode           
               ESC >           Numeric keypad mode 
               ESC F           Select graphics set
               ESC G           Select US character set
               ESC A           Move cursor up
               ESC B           Move cursor down
               ESC C           Move cursor right
               ESC D           Move cursor left
               ESC H           Home cursor
               ESC Y Pl Pc     Position cursor 
               ESC I           Reverse line feed
               ESC K           Erase to end of line
               ESC J           Erase to end of screen
               ESC Z           Identify -- response ESC / Z


        Cursor Keys
        -----------
        The  cursor  keys generate the following codes depending  on  the 
        cursor key mode which is set by a host application program and on 
        the emulation mode (VT100 or VT52). 

             Key      Cursor Mode Reset    Cursor Mode Set       VT52
            
            Up          ESC [ A              ESC O A            ESC A
            Down        ESC [ B              ESC O B            ESC B
            Right       ESC [ C              ESC O C            ESC C
            Left        ESC [ D              ESC O D            ESC D












        TERM 3.00  05/26/85                                  page 28

        TERMINAL EMULATION


        Numeric Keypad
        --------------
        The  keypad  on  the  right  side  of the  TI  PC  has  the  same 
        configuration as the VT100 keypad.   The top four keys on the  TI 
        PC  keypad  correspond  to the PF keys on the  VT100  keypad  and 
        always  generate  the PF key sequence.    The other  keypad  keys 
        either  generate their labeled code or a special escape  sequence 
        depending  on the alternate keypad mode set by a host application 
        program.   The keypad  keys  generate  the  following codes  when  
        in   alternate   keypad   mode and their  labeled  code  when  in 
        numeric  keypad  mode.   The emulation mode  (VT100,  VT52)  also 
        affects the escape sequence generated.


           KEY    VT100      VT52             KEY       VT100      VT52
            0    ESC O p    ESC ? p            9       ESC O y    ESC ? y
            1    ESC O q    ESC ? q            ,       ESC O l    ESC ? l
            2    ESC O r    ESC ? r            -       ESC O m    ESC ? m
            3    ESC O s    ESC ? s            .       ESC O n    ESC ? n
            4    ESC O t    ESC ? t            ENTER   ESC O M    ESC ? M
            5    ESC O u    ESC ? u        PF1 =       ESC O P    ESC P
            6    ESC O v    ESC ? v        PF2 +       ESC O Q    ESC Q
            7    ESC O w    ESC ? w        PF3 SPAC    ESC O R    ESC R
            8    ESC O x    ESC ? x        PF4 TAB     ESC O S    ESC S

                       Table of Numeric Keypad Codes


        Break Key
        ---------
        Pressing  shift-break will cause a short break to be sent.   This 
        is recognizable as an "attention" key on many systems.



























        TERM 3.00  05/26/85                                  page 29

        APPENDIX A    'C' Language characters



        'C' Language characters
        -----------------------

        Throughout TERM, when string parameters are requested, strings of 
        the  format used by the 'C' language may be specified.   In  'C', 
        strings  consist  of sequences of ASCII characters  with  special 
        control sequences mixed in.   The backslash character (\) is used 
        as an "escape" character to designate these control sequences.

        The control sequences consist of a backslash (\) followed by:

                  r    Carriage Return (CR)
                  n    Line Feed (LF)
                  f    Form Feed (FF)
                  b    Back Space (BS)
                  t    Tab (HT)

                  x    A special case which allows entering the 
                       hexidecimal   value  of  the   character       
                       directly.   The  'x'  is followed by two 
                       hex  digits.   For example,  \x0d  is  a 
                       carriage return (also \r).
                                     
        Also  any characters which may be interpreted as delimeters  such 
        as backslash, or quotation marks.  These are entered in a similar 
        fashion  as  backslash followed by the character (\\ would  be  a 
        translated to a single backslash).































        TERM 3.00  05/26/85                                  page 30