The Stack and Other Registers
                              Section II.

Complex calculations can be done easily with TexSolver-10 because
intermediate results are automatically stored and returned in the
"stack" registers.  This significantly reduces the number of keystrokes
needed to evaluate mathematical expressions.  This section explains the
usage of the stack registers and also the LAST X, storage, and LAST OP
registers.

                               The Stack

The stack consists of registers X, Y,Z, and T. The stack contents are
always displayed.  Any number keyed in or resulting from execution of a
function is placed in the X register. Depending upon the type of
operation performed, the stack contents will lift, drop, or remain the
same.  For example, number entry lifts the stack, one-number functions
do not alter stack positions, and two-number functions cause the stack
to drop.

                            Stack Functions

ENTER. After a number is keyed in, pressing ENTER indicates that one
number is finished being keyed in and prepares the calculator to accept
the next one.  When ENTER is pressed, the stack is lifted, that is, X
is copied to Y, Y to Z, Z to T, and T is lost.

R (Rotate Down, SHIFT-P) rotates the stack register contents down one
register. T is copied to Z, Z to Y, Y to X, and X to T.

XY (X exchange Y, SHIFT-O) exchanges the numbers in the X and Y
registers.

                  One-Number Functions and the Stack

One-number functions operate only on the number in the X register.  The
Y, Z, and T registers are not altered when a one-number function is
executed.  Examples of one-number functions are 1/X and X^2.

                   Two-Number Functions and the Stack

Functions that operate on two numbers require that the first number be
positioned in the Y register and the second number in the X register.
The result is placed in the X register and the stack drops after the
function is executed, that is, T is copied to Z, and Z to Y.  This
facilitates chain calculations.  Examples of two-number functions are +
and Y^X.

                                 LAST X

In addition to the four stack registers, there is also a separate
register, the LAST X register.  When most functions are executed, a
copy of the previous X register value is stored in the LAST X
register.  If desired, this value can then be restored to the X
register using the LAST X function (CTRL-X).  This feature allows the
number to be reused without reentering it.  Examples of operations that
store the old X value in LAST X are * and ûX. Examples of operations
that do not are ENTER and STO, since X is not modified.

                      Storage Register Operations

In addition to the stack and LAST X registers, 100 separate data
storage registers, numbers 00 to 99, are available.

STO (Store).  When this function is executed (SHIFT-I), you are
prompted to key in a two-digit number (00 to 99) to indicate a storage
register.  The X register value is then copied to the specified
register.

RCL (Recall).  When executed (CTRL-I) and followed by a storage
register number (00 to 99), a copy of the specified register value is
placed in the X register.

Storage Register Arithmetic.  Arithmetic can be performed on the
contents of a storage register with the result placed in the storage
register. To do this, execute STO (SHIFT-I) followed by an arithmetic
operator (+, -, *, /), followed by a storage register number (00 to
99). For example, pressing SHIFT-I / 21 divides the value in register
21 by the value in X and stores the result in register 21.

                                LAST OP

The LAST OP (Last Operation) register displays the most recently
performed operation.

                         Clearing the Registers

CLRG (Clear Registers, CTRL-P) clears the contents of all storage
registers, the stack, and LAST X to zero.