TI-PC and the IBM-PC ROM BIOS Conversion List


                     *****************************
                     **         I   CRT         **
                     *****************************

              TI PC                               IBM PC

    CRT DSR..........INT 49             Video I/O..........INT 10
Section 4.10 of the Tech Ref Man     Page 43 of the IBM BIOS Listing

    If the AH Register is:              If the AH Register is:

AH=00  Null Function               AH=00  Set Mode

AH=01  Set Cursor Type             AH=01  Set Cursor Type
    Both computers use the CX Register to set the Cursor Type. The 
                 IBM can not disable the Cursor Blink.

AH=02  Set Cursor Position         AH=02  Set Cursor Position
    DH=COLUMN Location of Cur.          DH=ROW Location of Cursor
    DL=ROW Location of Cursor           DL=COLUMN Location of Cur.

NOTE: The ROW/COLUMN designation has changed and the TI PC doesn't need 
to set the page number like the IBM PC does. 

AH=03  Read Cursor Position        AH=03  Read Cursor Position
    DH=COLUMN Location of Cur.          DH=ROW Location of Cursor
    DL=ROW Location of Cursor           DL=COLUMN Location of Cur. 

NOTE:  The ROW/COLUMN designation has changed and the CX Register is 
initialized with the same data. The TI-PC does not set the page number.

AH=04  Null Function               AH=04  Read Light Pen Position

AH=05  Null Function               AH=05  Select Active Display Page

AH=06  Scroll Text UP              AH=06  Scroll Page UP
    AL=0: Move Block                    AL=0:  Blank Entire Screen
    AL>0: Copy Block                    AL>0:  No of lines blanked at the 
                                               bottom of the screen
    BH,BL: Destination begin            BH:    Attribute used on a blank
           (COL/ROW Location)                  line
                                        BL:    Not used
    CH,CL: COL/ROW Length of            CH,CL: ROW/COL of Upper Left
           Block                               corner of Block
    DH,DL: Source begin COL/            DH,DL: ROW/COL of Lower Right
           ROW Location                        corner of Block

NOTE: The ROW/COLUMN designation is changed in the CX and DX Registers

AH=07  Scroll Text DOWN            AH=07  Scroll Page DOWN
                         Same as the Scroll UP

AH=08  Read Char & Attribute at    AH=08  Read Char & Attribute at
       current Cursor position            current Cursor position

AH=09  Write Char & Attribute at   AH=09  Write Char & Attribute at
       current Cursor position            current Cursor position
       The AL, BL, and CX Registers are initialized the same on
         both computers. The BH Reg is not used by the TI-PC.

AH=0A  Write Character only at     AH=0A  Write Character only at
       current Cursor position            current Cursor position
        The AL and CX Registers are the same for both computers

AH=0B  Null Function               AH=0B  Set Color Palette

AH=0C  Null Function               AH=0C  Write Dot

AH=0D  Null Function               AH=0C  Read Dot

AH=0E  Write ASCII Teletype        AH=0E  Write Teletype
    AL: Character to write              AL: Character to write
                                        BL: Foreground color (Graphics
    BX Register is not used                 Mode)
                                        BH: Display page in alpha mode

AH=0F  Null Function               AH=0F  Return current Video State


                     *****************************
                     **      II  KEYBOARD       **
                     *****************************

              TI-PC                               IBM-PC

    Keyboard DSR..........INT 4A        Keyboard I/O..........INT 16
Sect 4.12 of the Tech Ref Manual   Page 23 of the IBM BIOS Listing

    If the AH Register is:              If the AH Register is:

AH=00  Read Keyboard INPUT         AH=00  Read Keyboard INPUT
         Both Computers place the Character in the AL Register

AH=01  Read Keyboard STATUS        AH=01  Read Keyboard STATUS
                    Both Computers operate the same

AH=02  Read Keyboard MODE          AH=02  Return the current Shift Status
                  Mode is returned in the AL Register

AH=03  Flush Keyboard Buffer       AH=03  Null Function

AH=04  Keyboard OUTPUT             AH=04  Null Function

AH=05  Put Character into          AH=05  Null Function
       Keyboard Buffer


                     *****************************                        
                     **      III  PRINTER       **
                     *****************************

              TI-PC                               IBM-PC

    Print DSR..........INT 4B           Print I/O..........INT 17
Section 4.13 of the Tech Ref Man   Page 42 of the IBM BIOS Listing

AH=00  OUTPUT Character in AL      AH=00  OUTPUT Character in AL
                         Both operate the same

AH=01  Initialize the Printer      AH=01  Initialize the Printer 
                         Both operate the same

AH=02  Return Printer Status       AH=02  Read Printer Status
        Both operate the same but the status bits are different


                     *****************************
                     **        IV  DISK         **
                     *****************************

              TI-PC                               IBM-PC

    Disk DSR..........INT 4D            Diskette I/O..........INT 13
Section 4.11 of the Tech Ref Man   Page 32 of the IBM BIOS Listing

    If the AH Register is:              If the AH Register is:

AH=00  Reset Disk System           AH=00  Reset Disk System
                 Both reset the disk to a known state

AH=01  Return Status Code          AH=01  Read Status
    Both operate the same and return the status in the AL Register

         The following is a list of the Registers used in the

                    READ/WRITE/ VERIFY/FORMAT DSR:
                   DL - Drive Number (0-3)
                   DH - Track (Surface) Number (0-1)
                   CH - Cylinder Number (0-39)
                   CL - Sector Number (1-8)
                   AL - Number of Sectors
                   ES:BX - Segment:Offset of Buffer

AH=02  Read Sectors                AH=02  Read Sectors

AH=03  Write Sectors               AH=03  Write Sectors

AH=04  Verify Sectors              AH=04  Verify Sectors

AH=05  Format Track                AH=05  Format Track
            For each of the READ/WRITE/VERIFY/FORMAT DSR's
             the operation is the same for both computers

AH=06  Verify Data                 AH=06  Null Function

AH=07  Return ReTry Status         AH=07  Null Function

AH=08  Set Standard Disk           AH=08  Null Function
       Interface Table (DIT)
       for the unit

AH=09  Set DIT address for the     AH=09  Null Function
       unit

AH=0A  Return DIT address for      AH=0A  Null Function
       the unit

AH=0B  Turn OFF Diskette Drive     AH=0B  Null Function
       Motors

                     *****************************
                     **  V  TIME-OF-DAY CLOCK   **
                     *****************************

              TI-PC                               IBM-PC

    Time-of-Day Clock DSR..INT 4E       Time of Day Call.....INT 1A
Section 4.9 of the Tech Ref Man    Page 77 of the IBM BIOS Listing

    If the AH Register is:              If the AH Register is:

AH=00  Set the Date                AH=00  Read the current clock settings
    BX: The Date                        AL: 24 Hour Indicator
                                        CX: High portion of count
                                        DX: Low portion of count

AH+01  Set the Time                AH+01  Set the Current Clock
                         Both operate the same

AH=02  Get the Date & Time         AH=02  Null Function


                     *****************************
                     **   VI  8259 INTERRUPTS   **
                     *****************************

              TI-PC                               IBM-PC

8259 INT (TIMER)........INT 43     8259 INT (0) Timer......INT 8
8259 INT 6 (Disk Cont)..INT 46     8259 INT (6) Diskette...INT E
8259 INT 7 (Keyboard)...INT 47     8259 INT (1) Keyboard...INT 9
8259 INT Vectors 0, 1, 2, 4, 5     8259 INT Vectors 2, 3, 4, 5, 7
    are not used on the TI PC           are not used on the IBM PC
                     *****************************
                     ** VII  INTERRUPT VECTORS  **
                     *****************************

       The Interrupt Vectors 0-4 are the same on both Computers


                     *****************************
                     **       VIII  OTHER       **
                     *****************************

Keyboard Print Screen.....INT 5E   Print Screen..........INT  5
Memory Size...............INT 66   Memory Check..........INT 12
System Config Call........INT 4F   Equipment Check.......INT 11

        The Following TI Interrupts are not used on the IBM PC
    Speaker DSR..................................INT 40
    Clock & Analog Interface Board...............INT 4C
    System Configuration.........................INT 4F
    Fatal Software Error.........................INT 50
    Restart Timing Event.........................INT 51
    Cancel Timing Event..........................INT 52
    Service Interfacing Subroutine...............INT 53
    Activate Task Subroutine.....................INT 54
    Reserved for Future Use......................INT 55 & 56
    CRT Mapping Vector...........................INT 57
    System Timing, 25ms..........................INT 58
    Common Interrupt Exit Vector.................INT 59
    System Timing, 100ms.........................INT 5A
    Keyboard Mapping Vector......................INT 5B
    Keyboard Program Pause Key Vector............INT 5C
    Keyboard Program Break Key Vector............INT 5D
    Keyboard Queuing Vector......................INT 5F
    ROM Pointers.................................INT 60 - 65

        The Following IBM Interrupts are not used by the TI PC
    RS232 I/O Call...............................INT 14
    Cassette I/O Call............................INT 15
    ROM Basic Entry Code.........................INT 18
    Boot Strap Loader............................INT 19
    Get Control on Keyboard Break................INT 1B
    Get Control on Timer Interrupt...............INT 1C
    Pointer to Video Initialization Table........INT 1D
    Pointer to Diskette Parameter Table..........INT 1E
    Pointer to Table for Graphics Char Gen.......INT 1F

          **************************************************
          **     IX  DOS CALLS & HIGH LEVEL LANGUAGES     **
          **************************************************

    The DOS Interrupts (INT 20-3F) and Function Calls are identical on 
both computers. For High Level languages (FORTRAN, PASCAL, etc) the 
object code should be compatable as long as you did not interface with 
assembly language. If you did, convert your assembly language code.